## Slide 1: System Identification within Flight Test and Flight Physics
18.04.2018
A project proposal
Alejandro Valverde
Notes: Hello everyone, my name is Alejandro Valverde and I have an idea. Idea which I would like to propose to you today.
What I am going to introduce now is not entirely the result of my own work, but it incorporate valuable feedback that I have receive from different people in this company over the last few days.
For those of you already initiated in this topic, I would like to implement System ID techniques into the current Flight Testing methodology. I would do this in a:
Cost effective,
Efficient, and
Accurate,
ways. And in this presentation, I will describe how I want to do this.
Now, for those of you not initiated in this topic…

## Slide 2: Aircraft System Identification
@ Kopter Group AG | Alejandro Valverde
System Identification is the process of building mathematical models for physical systems based on imperfect observations or measurements
When applied to aircraft, it is called Aircraft System Identification
Notes: One of the oldest and most fundamental of all human scientific pursuits is developing mathematical models for physical systems based on imperfect observations or measurements. This activity is known as system identification. When applied to aircraft, this is known as aircraft system identification.
And this is in fact one of the reasons why I am so interested in this topic, This discipline is fairly unknown in the aerospace industry, but it is in fact something that scientists and engineers have been doing for hundreds of years.
I like to recall know the contribution to human progress made by Johannes Kepler when, in 1609, he published the book Astronomia nova which presented a mathematical model that describe the motion of the planets in the Solar System. For this, he collaborated with the Swedish Tycho Brahe, who provided him with precise data of planets position in the sky. This was System Identification.

## Slide 3: Problems in Aircraft Dynamics
@ Kopter Group AG | Alejandro Valverde
Input, u
System, S
Output, z
Simulation: Given u and S, find z
Control: Given z and S, find u
Identification: Given z and u, find S
Notes: Now, in our company, we have already covered some of the classical problems of Aircraft Dynamics.
Simulation: This is what the guys from Flight Physics do when they use FlightLab
Control: This is what our pilot does in his brain.. Since, we don’t have yet developed an autopilot, we don’t need to worry too much about this point.
Identification: Here is when we obtain a model for our helicopter, considering both the input and output to the model.
For Kepler, this box was occupied by the solar system, for us this is the SH09; but in fact it same. Well, in fact, poor Kepler’s task was harder than ours because he did have control over the inputs to the system and we do have.

## Slide 4: Applications of Aircraft System ID techniques
@ Kopter Group AG | Alejandro Valverde
Aircraft System Identification offers a wide range of different applications, including:
Flight Simulator development
Flight envelope expansion
Flight Control System (FCS) design
Handling Qualities assessment
and enhancement
And many others…
Notes: Flight Simulator development: When we require an accurate representation of the aircraft in all the flight conditions. Many aircraft motions and flight conditions simply cannot be duplicated in the wind tunnel nor computed analytically with sufficient accuracy or computational efficiency
Flight Envelope Expansion: Quantifying stability and control impact of aircraft modifications, configuration changes, or special flight conditions;
Flight Control Systems Stability augmentation and flight control systems. This is essential requirement for certain flight conditions such as night flying and others low-visibility conditions (acc. to Michael, Kopter Flight Test pilot). (It is needed to consider the models limitations and the type of aerodynamic effects.)

## Slide 5: Aircraft Simulation - Ongoing Kopter project
@ Kopter Group AG | Alejandro Valverde
Extracted from Nicolas Callejo’s MSc Thesis overview in collaboration with Kopter Avionics Dep.
Example of SID implementation

## Slide 6: Aircraft Simulation – Current Kopter approach
@ Kopter Group AG | Alejandro Valverde
Trimmed condition of FlightLab, e.g.:
fwd level flight @ 100kts
linearization of full H/C dynamics in LTI model:
Non-linear model
Linear model
Suitable for:
FCS design
H/C flight simulation
Aircraft dynamic stability analysis
Dynamic Simulation

## Slide 7
@ Kopter Group AG | Alejandro Valverde
System ID provides an accurate, simple and reliable
model of the H/C dynamics obtained from real flight test data of the real H/C
LUTs
LPV model
…
Equations of Motion
Dynamic Simulation
Aerodynamic, structural and propulsive H/C model
Pilot inputs
Forces: Moments:
Aircraft Simulation – Aircraft SID approach
Non-linear model
In the form of
Notes: Accurate -> Because it’s based on real flight data
Simple -> Does not require high computational power
Reliable -> Computed with

## Slide 8: System ID R/C Model vs FlightLab
@ Kopter Group AG | Alejandro Valverde
Advantages:
High accuracy provided that good quality data points are available
Validation -> instantaneous
Non-linear flight dynamics
Transient flight conditions
Real-time dynamic modelling
Account for aeroelastic effects
Drawbacks:
Depend on flight test data availability and dedicated flight manoeuvres
Advantages:
Not dependent on flight test data
Model complexity adjustable: Full aeroelastic -> loads&dynamics Rigid -> flight mechanics
Drawbacks:
Validation -> complicated
Full aeroelastic model -> complicated
Internal parameters hard to properly be tuned
FlightLab H/C model
H/C model from System ID
Best use: Prediction of H/C:
- H/C and compnt. loads
- Rotor dynamics
- H/C Performance
Best use: Dynamic model of the real H/C: - FCS design - Handling qualities - Simulator development
Notes: Flightlab can be used also for evaluate helicopter design changes impact or for the preliminary design of a new vehicle,
identified model cannot be used to infer anything about a vehicle different from which was tested and identified.

## Slide 9: How does it work?
@ Kopter Group AG | Alejandro Valverde
Forces and moments
Develop a model form from which parameters can be estimated using flight test data
for example
static stability
dynamic stability (damping)
pitch control authority
pitching moment bias
H/C angle of attack
longitudinal angular velocity
pitch control input
Pitching moment coefficient
measurement noise

## Slide 10: How does it work?
@ Kopter Group AG | Alejandro Valverde
Pitching moment model:
SID Model:
Model output
Regresors
Values of variables measured
Observations
Noise of the measurement
Vector of regressors (parameters to be identified)
Observations
- Simple
- Real time parameters estimations
Equation-Error
two approaches
Output-Error
Solved in one-shot linear algebra
Solved with iterative nonlinear optimization
- Any nonlinear system dynamics
- Machine learning techniques
Notes: NOTES
The coefficients of the Taylor series expansion are the aero-dynamic model parameters to be estimated. These parameters are therefore a function of flight condition for the test.

## Slide 11: Tools – SIDPAC software
@ Kopter Group AG | Alejandro Valverde
No development time needed
Collection of over 350 state-of-the-art programs
Used at more than 80 organization worldwide
Implemented in Matlab

## Slide 12: Tools – SIDPAC software
Measured inputs:
- -
Outputs to be validated against real flight test data:
-
SID H/C Model

## Slide 13: What would we need?
@ Kopter Group AG | Alejandro Valverde
Complete instrumented helicopter
Flight Test operations
We already have this
- IMUs
- MR/TR rpm
-
- …
Flight Physics
SID framework development
Dedicated flight test points
Data to be provided by Flight Test Data Analysis Team
Some of those they may already be within the current Flight Test Program
Little involvement needed as data in raw form is analysed for SID methods
SIDPAC embedding within current analysis tool
Specific code to be written to handle flight P3 test data
Notes: According to Lemke:
Do not underestimate resources
  Having one person full dedicated to this project
  Requirements to Flight Test Data analysts
    Maybe I don’t require a lot from them. I would need to work directly from the raw data, unfiltered
    Data portioning can be easily done as pre-processing prior the SID parameter estimation
    Filtering should not be done analogy, as in most of the cases, no a priori knowledge of the frequency band of interest
    It is preferred to use post-flight data smothering techniques such as
      Frequency-Domain Filter Implemented in the Time Domain
      Local Smoothing in the Time Domain
      Global Smoothing in the Frequency Domain

## Slide 14: Instrumentation overview
Physical quantities to measure | Variables | Units | Transducer | Notes
Air-Relative Velocity |  |  | Pressure transducer Flow vane | Difficult to measure (local flow interaction)
Angular Velocity |  |  | Rate gyro | -
Translational accelerations |  |  | Accelerometer | Noisy measurements
Rotational acceleration |  |  | Rate acceleration gyro | Optional, can be differentiated from velocities
Euler attitude angles |  |  | Vertical gyro | Optional, include gravity
Pilot controls |  |  | Potentiometer | -
Physical quantities to measure | Variables | Units | Transducer | Notes
Air-Relative Velocity |  |  | Pressure transducer Flow vane | Difficult to measure (local flow interaction)
Angular Velocity |  |  | Rate gyro | -
Translational accelerations |  |  | Accelerometer | Noisy measurements
Rotational acceleration |  |  | Rate acceleration gyro | Optional, can be differentiated from velocities
Euler attitude angles |  |  | Vertical gyro | Optional, include gravity
Pilot controls |  |  | Potentiometer | -
Notes: Air-Relative Velocity
It doesn’t matter where this sensors are placed in the helicopter. There always be corrections to be made.

## Slide 15: Inputs
Dedicated flight test maneuvers are needed:
In any case, most of the necessary maneuvers already belong to the flight test program as part of the handling qualities assessment
Notes: -> Two runs with the same inputs for data analysis

## Slide 16: Implementation stages, overview
Development of the SID framework suitable for flight test data
FCS design
P3 flight test data
Evaluation of SID possibilities for SH09
Flightlab linearized model
Simulation development
Integration of SID routine with Flightlab
Flightlab nonlinear model
Optimization of Flightlab parameters to match flight data
SID framework development
Development of essential technology
Flightlab
validation

## Slide 17: Implementation stages, detailed view
@ Kopter Group AG | Alejandro Valverde
Perform first approach System ID on FlightLab:
Rigid body System ID framework using FlightLab linearized model
Inclusion of simulated disturbances in the measurements
Develop a System ID framework suitable for real flight test data:
Rigid body System ID framework
Use of P2 flight test data if suitable
Provide dynamic model of P2 suitable for:
  FCS design
  Simulator development
Assist P3 flight envelope expansion in Sicily:
Developed System ID framework could be ready to:
  Perform post-flight analysis for accurate parameter estimation
  Real-time dynamic modelling
Address handling qualities issues
April
Beginning of summer
Beginning of summer
…
Embedment of SID within on FlightLab:
Optimization of Flightlab parameters to match flight data
Notes: First phase:
We can start approaching the problem using the simplest available model in Flightlab (MR and TR rigid, fuselage rigid) and generate linearized model at different trim flight condition and W/CG configuration, to be used for identification.
Second phase:
We can integrate the identification routine with Flightlab (it implies non-trivial software engineering effort in order to call Flightlab runs from Matlab) working directly in the non-linear environment, optimizing directly some parameters of the Flightlab model to match the flight data.

## Slide 18: Why to introduce System ID into P3 test campaign?
@ Kopter Group AG | Alejandro Valverde
We have to do it now,
we are ready now
System ID takes time and money – but not nearly as much as not doing it Eugene A. Morelli NASA Langley Research Center Hampton
Assist P3 flight envelope expansion in Sicily, necessary for TC. Issues like the cyclic migration could be addressed and main driving parameters identified.
Surely it will be needed for PS4 and further
developments after TC, such as FCS and SAS design
Cost effective
Provide a proper dynamic model of the H/C
for the simulator
Sooner or later, it would need to be implemented
Every big helicopter manufacturer has a dedicated SID department
Validation of Flightlab model. SID would provide the necessary bridge between the software and real flight test data.
Notes: Cyclic migration.. Identify driving parameters of this behavior and properly address it.
In my vision, P3 flights (some fractions of) could be used to collect data for SID, and in the meantime the tool can be developed. Providing a robust and reliable software for this scope is not a simple thing and requires a lot of time!

## Slide 19: Why I can be the one doing this?
@ Kopter Group AG | Alejandro Valverde
I know what to do and how to do it
Kopter experience, within rotorheads
Data analysis experience
Python
Matlab
Data analysis and machine learning techniques
…
Young
Passionate

## Slide 20: First steps already taken, using SIDPAC and Flightlab
@ Kopter Group AG | Alejandro Valverde
73 states
6 outputs
4 inputs
fwd level flight
147 kts
2800 kg
= 3.37m
LTI model

## Slide 21
@ Kopter Group AG | Alejandro Valverde

## Slide 22: Thank you

## Slide 23: References
@ Kopter Group AG | Alejandro Valverde

## Slide 24: System ID methodology diagram
@ Kopter Group AG | Alejandro Valverde
Optimized Input
Data Collection & Compatibility
Estimation Algorithm / Optimization
Identification Criteria
Helicopter
Mathematical Model / Simulation
+
-
Input
Actual Response (training dataset)
Model Response
Response Error
A Priori Values, lower/upper bounds
Model structure
Model Validation
Parameter Adjustments
Identification Phase
Validation Phase
Complementary Flight Data (validation dataset)
Parameter Estimation
Manoeuvre
Measurements
Methods
Models

## Slide 25: Inputs
Constraints on inputs:
Rate of data acquisition
Limited resolution on sensors or data acquisition system
Limited time for each maneuver
Limitations on how the aircraft can be excited
Notes: Manoeuvre definition:
  Manoeuvre time length,
  Control surfaces or pilot inputs to be moved,
  Input forms (e.g., square wave, frequency sweep, etc.), which includes the input amplitudes.