## Slide 1: System Identification within Flight Test and Flight Physics
02.03.2018
A project proposal
Alejandro Valverde
Notes: Hello everyone, my name is Alejandro Valverde and I have an idea. Idea which I would like to propose to you today.
What I am going to introduce now is not entirely the result of my own work, but it incorporate valuable feedback that I have receive from different people in this company over the last few days.
For those of you already initiated in this topic, I would like to implement System ID techniques into the current Flight Testing methodology. I would do this in a:
Cost effective,
Efficient, and
Accurate,
ways. And in this presentation, I will describe how I want to do this.
Now, for those of you not initiated in this topic…

## Slide 2: Aircraft System Identification
@ Kopter Group AG | Alejandro Valverde
System Identification is the process of building mathematical models for physical systems based on imperfect observations or measurements
When applied to aircraft, it is called Aircraft System Identification
Notes: One of the oldest and most fundamental of all human scientific pursuits is developing mathematical models for physical systems based on imperfect observations or measurements. This activity is known as system identification. When applied to aircraft, this is known as aircraft system identification.
And this is in fact one of the reasons why I am so interested in this topic, This discipline is fairly unknown in the aerospace industry, but it is in fact something that scientists and engineers have been doing for hundreds of years.
I like to recall know the contribution to human progress made by Johannes Kepler when, in 1609, he published the book Astronomia nova which presented a mathematical model that describe the motion of the planets in the Solar System. For this, he collaborated with the Swedish Tycho Brahe, who provided him with precise data of planets position in the sky. This was System Identification.

## Slide 3: Problems in Aircraft Dynamics
@ Kopter Group AG | Alejandro Valverde
Input, u
System, S
Output, z
Simulation: Given u and S, find z
Control: Given z and S, find u
Identification: Given z and u, find S
Notes: Now, in our company, we have already covered some of the classical problems of Aircraft Dynamics.
Simulation: This is what the guys from Flight Physics do when they use FlightLab
Control: This is what our pilot does in his brain.. Since, we don’t have yet developed an autopilot, we don’t need to worry too much about this point.
Identification: Here is when we obtain a model for our helicopter, considering both the input and output to the model.
For Kepler, this box was occupied by the solar system, for us this is the SH09; but in fact it same. Well, in fact, poor Kepler’s task was harder than ours because he did have control over the inputs to the system and we do have.

## Slide 4: Applications of Aircraft System ID techniques
@ Kopter Group AG | Alejandro Valverde
Aircraft System Identification offers a wide range of different applications, including:
Flight Simulator development
Flight envelope expansion
Flight Control System (FCS) design
Handling Qualities assessment
and enhancement
And many others…
Notes: Flight Simulator development: When we require an accurate representation of the aircraft in all the flight conditions. Many aircraft motions and flight conditions simply cannot be duplicated in the wind tunnel nor computed analytically with sufficient accuracy or computational efficiency
Flight Envelope Expansion: Quantifying stability and control impact of aircraft modifications, configuration changes, or special flight conditions;
Flight Control Systems Stability augmentation and flight control systems. This is essential requirement for certain flight conditions such as night flying and others low-visibility conditions (acc. to Michael, Kopter Flight Test pilot). (It is needed to consider the models limitations and the type of aerodynamic effects.)

## Slide 5: Aircraft Simulation - Ongoing Kopter project
@ Kopter Group AG | Alejandro Valverde
Extracted from Nicolas Callejo’s MSc Thesis overview in collaboration with Kopter Avionics Dep.

## Slide 6: Aircraft Simulation – Current Kopter approach
@ Kopter Group AG | Alejandro Valverde
Trimmed condition of FlightLab, e.g.:
fwd level flight @ 100kts
linearization of full H/C dynamics in LTI model:
Non-linear model
Linear model
Suitable for:
FCS design
H/C flight simulation
Aircraft dynamic stability analysis
Dynamic Simulation

## Slide 7
@ Kopter Group AG | Alejandro Valverde
System ID provides an accurate, simple and reliable
model of the H/C dynamics obtained from real flight test data of the real H/C
LUTs
LPV model
…
Equations of Motion
Dynamic Simulation
Aerodynamic, structural and propulsive H/C model
Pilot inputs
Forces: Moments:
Aircraft Simulation – Aircraft SID approach
Non-linear model
In the form of
Notes: Accurate -> Because it’s based on real flight data
Simple -> Does not require high computational power
Reliable -> Computed with

## Slide 8: System ID R/C Model vs FlightLab
@ Kopter Group AG | Alejandro Valverde
Advantages:
High accuracy provided that good quality data points are available
Validation -> instantaneous
Non-linear flight dynamics
Transient flight conditions
Real-time dynamic modelling
Account for aeroelastic effects
Drawbacks:
Depend on flight test data availability and dedicated flight manoeuvres
Advantages:
Not dependent on flight test data
Model complexity adjustable: Full aeroelastic -> loads&dynamics Rigid -> flight mechanics
Drawbacks:
Validation -> complicated
Full aeroelastic model -> complicated
Internal parameters hard to properly be tuned
FlightLab H/C model
H/C model from System ID
Best use: Prediction of H/C:
- H/C and compnt. loads
- Rotor dynamics
- H/C Performance
Best use: Dynamic model of the real H/C: - FCS design - Handling qualities - Simulator development
Notes: Flightlab can be used also for evaluate helicopter design changes impact or for the preliminary design of a new vehicle,
identified model cannot be used to infer anything about a vehicle different from which was tested and identified.

## Slide 9: How does it work?
@ Kopter Group AG | Alejandro Valverde
Forces and moments
Develop a model form from which parameters can be estimated using flight test data
for example
static stability
dynamic stability (damping)
pitch control authority
pitching moment bias
H/C angle of attack
longitudinal angular velocity
pitch control input
Pitching moment coefficient
measurement noise

## Slide 10: How does it work?
@ Kopter Group AG | Alejandro Valverde
Pitching moment model:
SID Model:
Model output
Regresors
Values of variables measured
Observations
Noise of the measurement
Vector of regressors (parameters to be identified)
Observations
- Simple
- Real time parameters estimations
Equation-Error
two approaches
Output-Error
Solved in one-shot linear algebra
Solved with iterative nonlinear optimization
- Any nonlinear system dynamics
- Machine learning techniques

## Slide 11: Tools – SIDPAC software
@ Kopter Group AG | Alejandro Valverde
No development time needed
Collection of over 350 state-of-the-art programs
Used at more than 80 organization worldwide
Implemented in Matlab

## Slide 12: Tools – SIDPAC software
Measured inputs:
- -
Outputs to be validated against real flight test data:
-
SID H/C Model

## Slide 13: What would we need?
@ Kopter Group AG | Alejandro Valverde
We already have this
Complete instrumented helicopter
A laptop
Some coffee…
- IMUs
- MR/TR rpm
-
- …

## Slide 14: Instrumentation overview

## Slide 15: Inputs
Constraints on inputs:
Rate of data acquisition
Limited resolution on sensors or data acquisition system
Limited time for each maneuver
Limitations on how the aircraft can be excited

## Slide 16: Inputs

## Slide 17: Why to introduce System ID into P3 test campaign?
@ Kopter Group AG | Alejandro Valverde
We have to do it now,
we are ready now
System ID takes time and money – but not nearly as much as not doing it Eugene A. Morelli NASA Langley Research Center Hampton
Assist P3 flight envelope expansion in Sicily, necessary for TC. Issues like the cyclic migration could be addressed and main driving parameters identified.
Surely it will be needed for PS4 and further
developments after TC, such as FCS design
Cost effective
Provide a proper dynamic model of the H/C
for the simulator
Sooner or later, it would need to be implemented
Every big helicopter manufacturer has a dedicated SID department
SID framework could be developed now using P2 flight test data
Notes: About Morelli:
Definitely explain who E. Morelli is.. NASA's go to guy for System Identification.. I like the story about the hypersonic vehicle that the US flew from somewhere off the west coast of the USA, where the craft took 13 minutes to reach Australia.. Morelli was given 30 seconds of that 13 minutes to put inputs into the control surfaces in order to assess the flight dynamics
Cyclic migration.. Identify driving parameters of this behavior and properly address it.

## Slide 18: Why I can be the one doing this?
@ Kopter Group AG | Alejandro Valverde
I know what to do and how to do it
Kopter experience, within rotorheads
Data analysis experience
Python
Matlab
Data analysis and machine learning techniques
…
Young
Passionate
Availability from April onwards

## Slide 19: Next steps – Near future
@ Kopter Group AG | Alejandro Valverde
Perform first approach System ID on FlightLab:
  Rigid body System ID framework
  FlightLab linearized model
  Inclusion of simulated disturbances in the measurements
Develop a System ID framework suitable for real flight test data:
  Rigid body System ID framework
  Use of P2 flight test data if suitable
  Assessment of handling qualities issues
  Inclusion of aeroelastic effects
  Provide dynamic model of P2 suitable for:
    FCS design
    Simulator development
Assist P3 flight envelope expansion in Sicily:
  Developed System ID framework could be ready to:
    Perform post-flight analysis for accurate parameter estimation
    Real-time dynamic modelling
  Address handling qualities issues
April
Beginning of summer
Beginning of summer
…

## Slide 20: First steps, using FlightLab
@ Kopter Group AG | Alejandro Valverde
73 states
6 outputs
4 inputs
fwd level flight
147 kts
2800 kg
= 3.37m
LTI model

## Slide 21
@ Kopter Group AG | Alejandro Valverde

## Slide 22: Thank you

## Slide 23: References
@ Kopter Group AG | Alejandro Valverde

## Slide 24: System ID methodology diagram
@ Kopter Group AG | Alejandro Valverde
Optimized Input
Data Collection & Compatibility
Estimation Algorithm / Optimization
Identification Criteria
Helicopter
Mathematical Model / Simulation
+
-
Input
Actual Response (training dataset)
Model Response
Response Error
A Priori Values, lower/upper bounds
Model structure
Model Validation
Parameter Adjustments
Identification Phase
Validation Phase
Complementary Flight Data (validation dataset)
Parameter Estimation
Manoeuvre
Measurements
Methods
Models