## Slide 1: System Identification to support and enhance Flight Testing
23.02.2018
A project proposal
Alejandro Valverde
Notes: Hello everyone, my name is Alejandro Valverde and I have an idea. Idea which I would like to propose to you today.
For those of you already initiated in this topic, I would like to implement System ID techniques into the current Flight Testing methodology. I would do this in a:
Cost effective,
Efficient, and
Accurate,
ways. And in this presentation, I will describe how I want to do this.
Now, for those of you not initiated in this topic…

## Slide 2: Aircraft System Identification
@ Kopter Group AG | Alejandro Valverde
System Identification is the process of building mathematical models for physical systems based on imperfect observations or measurements
When applied to aircraft, it is called Aircraft System Identification
Notes: One of the oldest and most fundamental of all human scientific pursuits is developing mathematical models for physical systems based on imperfect observations or measurements. This activity is known as system identification. When applied to aircraft, this is known as system identification.
And this is in fact one of the reasons why I am so interested in this topic, This discipline is fairly unknown in the aerospace industry, but it is in fact something that scientists and engineers have been doing for hundreds of years.
I like to recall know the contribution to human progress made by Johannes Kepler when, in 1609, he published the book Astronomia nova which presented a mathematical model that describe the motion of the planets in the Solar System. For this, he collaborated with the Swedish Tycho Brahe, who provided him with precise data of planets position in the sky. This was System Identification.

## Slide 3: Problems in Aircraft Dynamics
@ Kopter Group AG | Alejandro Valverde
Input, u
System, S
Output, z
Simulation: Given u and S, find z
Control: Given z and S, find u
Identification: Given z and u, find S
Notes: Now, in our company, we have already covered some of the classical problems of Aircraft Dynamics.
Simulation: This is what the guys from Flight Physics do when they use FlightLab
Control: This is what our pilot does in his brain.. Since, we don’t have yet developed an autopilot, we don’t need to worry too much about this point.
Identification: Here is when we obtain a model for our helicopter, considering both the input and output to the model.
For Kepler, this box was ocuppaid by the solar universy, for us this is the SH09; but in fact it same. Well, in fact, poor Kepler’s task was harder than us becaue he did have control over the inputs to the system and we do have.

## Slide 5: Applications of Aircraft System ID techniques
@ Kopter Group AG | Alejandro Valverde
Aircraft System Identification offers a wide range of different applications, including:
Flight Simulator development
Flight envelope expansion
Evaluation of new aircraft
Handling Qualities assessment
and enhancement
And many others…
Picture of the flight simulator in the basement
Notes: Flight Simulator development:
Flight Envelope Expansion. (It is needed to consider the models limitations and the type of aerodynamic effects.)

## Slide 6: Aircraft Simulation - Ongoing Kopter project
@ Kopter Group AG | Alejandro Valverde
Extracted from Nicolas’ MSc Thesis overview in collaboration with Kopter Avionics Dep.

## Slide 7: Aircraft Simulation – Current Kopter approach
@ Kopter Group AG | Alejandro Valverde
Trimmed condition of FlightLab, e.g.:
fwd level flight @ 100kts
linearization of full H/C dynamics:
Non-linear model
Linear model
Suitable for:
FCS design
H/C flight simulation
Aircraft dynamic stability analysis
Dynamic Simulation

## Slide 8
@ Kopter Group AG | Alejandro Valverde
System ID provides an accurate, simple and reliable model of the H/C dynamics obtained from real flight test data of the real H/C
LUTs
Equations of Motion
Dynamic Simulation
Aerodynamic, structural and propulsive H/C model
Pilot inputs
Forces: Moments:
Aircraft Simulation – Current Kopter approach
Non-linear model
Notes: Accurate -> Because it’s based on real flight data
Simple -> Does not require high computational power
Reliable -> Computed with

## Slide 9: System ID R/C Model vs FlightLab
@ Kopter Group AG | Alejandro Valverde
Advantages:
High accuracy
Validation -> instantaneous
Non-linear flight dynamics
Transient flight conditions
Real-time dynamic modelling
Drawbacks:
Depend on flight test data availability
Advantages:
Not dependent on flight test data
Drawbacks:
Validation -> complicated
Only linear flight dynamics
FlightLab H/C model
H/C model from System ID
Best use: Loads prediction
Best use: Dynamic model of the
real H/C

## Slide 10: How does it work?
@ Kopter Group AG | Alejandro Valverde
Forces and moments
Develop a model form from which parameters can be estimated using flight test data
for example, using Taylor series expansion
static stability
dynamic stability (damping)
pitch control authority
pitching moment bias
H/C angle of attack
longitudinal angular velocity
pitch control input
Pitching moment coefficient

## Slide 11: How does it work?
@ Kopter Group AG | Alejandro Valverde
Pitching moment model:
Model:
Model output
Regresors
X: Values of variables measured
Observations
Noise of the measurement
Vector of regressors (parameters to be identified)
Observations
- Simple
- In flight on fly estimations
Equation-Error
two approaches
Output-Error
Solved in one-shot linear algebra
Solved with iterative nonlinear optimization
- Any nonlinear system dynamics
- Machine learning techniques

## Slide 12: Tools – SIDPAC software
@ Kopter Group AG | Alejandro Valverde
Already available
No development time needed
Proven industry suitable software
Further ways:
    Python implementation

## Slide 13: Tools – SIDPAC software

## Slide 15: What would I need?
some accelerometers installed in P3, a part from the usual instrumentation… -> we already have this
A laptop
Some coffee
@ Kopter Group AG | Alejandro Valverde

## Slide 16: Why to introducing System ID into P3 test campaign?
Sooner or later –> Every big helicopter manufacturer has SID implemented
Assist P3 flight envelope expansion
Provide a propor dynamic model of the H/C for the simulator
Cost effective
Surely it will be need for PS4 and further developments after TC
System ID takes time and money – but not nearly as much as not doing it Eugene A. Morelli NASA Langley Research Center Hampton
@ Kopter Group AG | Alejandro Valverde
We have to do it now,
we are ready now
Notes: About Morelli:
Definitely explain who E. Morelli is.. NASA's go to guy for System Identification.. I like the story about the hypersonic vehicle that the US flew from somewhere off the west coast of the USA, where the craft took 13 minutes to reach Australia.. Morelli was given 30 seconds of that 13 minutes to put inputs into the control surfaces in order to assess the flight dynamics

## Slide 17: Why I can be the one doing this?
Young <-> Passionate
I know what to do and how to do it
Kopter experience
Data analysis experience
        Python
        Matlab
        Data analysis and machine learning techniques
        …
@ Kopter Group AG | Alejandro Valverde

## Slide 18
@ Kopter Group AG | Alejandro Valverde

## Slide 19: Thank you

## Slide 20: References
[1]: Aircraft System Identification. Theory and Practice.
@ Kopter Group AG | Alejandro Valverde